Metering Notice and Within-Day Metering Notice

This section describes the exchange format for data relating to the Metering Notice, in short referred to as "AM”, and to the Within-Day Metring Notice, in short referred to as “AMJ”.

# FILE DEFINITION

The Metering Notice contains metering at Metering Points linked to PLC/PLCd for the gas day D.  It contains daily and hourly data. It is published once on day D+1.

The Within-Day Metering Notice contain hourly meterings at Metering Points linked to PLC/PLCd for the gas day D. It is published 5 times a day.

# WHERE TO FIND THE DOCUMENT(s)

The AM and AMJ files can be downloaded from the TRANS@ction web portal via the publication search page:

Lastly, the AM and AMJ files will also be accessible in B2B mode from ERMES.

# File name and format

The file is published in the CSV and XML formats.

It will be named according to the following rule:

| No. | Designation | Type | Length | Format |
| --- | --- | --- | --- | --- |
| 1 | Mode of exchange | Alphanumeric | 3 | AM ou AMJ |
| 2 | Contract code | Alphanumeric |  |  |
| 3 | Date | Date | 14 | DDMMYYYYHHmmSS |
| 4 | Extension | Alphanumeric | 4 | .csv ou .xml |
| 5 | Separators |  | 4 | « _ » |

In consequence, the final complete file name will be:

AM _ CODECONTRAT _JJMMAAAAHHmmSS.csv

AM _CODECONTRAT _JJMMAAAAHHmmSS.xml

Or

AMJ _ CODECONTRAT _JJMMAAAAHHmmSS.csv

AMJ _CODECONTRAT _JJMMAAAAHHmmSS.xml

# FILE Description

## CSV format

The tables presented in this section contain the following columns:

- No.: No. of field in the line

- Name: description of field content

- Type: type of field

- Length

- Unit

- Format: Data format.

- Compulsory: determines whether the field is mandatory or not; if not, the field is kept empty.

- Value: type of values specific to the data or example(s) of values.

- Comment: additional information.

In the following tables, the types of values are as follows:

- N: numeric

- X, AN: alphanumeric

- D: date

- H: time

- E: 1-character enumeration.

The length is given within brackets where applicable:

- X(n) is a sequence of n alphanumeric characters,

- 9(n) is a sequence of n numeric characters,

- S9(n) is a numeric sequence with sign + or -.

The decimal separator is a dot.

| No. | Name | Type | Length | Unit | Format | Compulsory | Value or Example | Comment |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Service data header (each part on 1 line) |
| 1 | LIBELLE_FLUX_FR | AN | X |  | LIBELLE_FLUX_FR / LIBELLE_FLUX_EN : CODE_FLUX-x | Y | Avis de mesures / Metering notice : AM-123456789 Or Mesures intra-journalières / Within-day metering notice : AMJ-123456789 | AM–x AMJ-x where x refers to an order number |
| 2 | RESEAU | AN | X |  | Text | Y | Réseau / Network : Gaz de France – Transporteur | Constant |
| 3 | Période / Period | D | X |  | DD/MM/YYYY HH:mm - DD/MM/YYYY HH:mm | Y | Période / Period : 01/07/2010 06:00 – 02/07/2010 05:59 | Beginning and end publication dates as follows : DD/MM/YYYY HH:mm - DD/MM/YYYY HH:mm |
| 4 | ID contrat / ID contract | AN | X |  | Text | Y | ID contrat / ID contract : GFxxxx01 | GRTgaz ref. no. for the contract |
| 5 | ID expéditeur / ID shipper | AN | X |  | Text | Y | ID expéditeur / ID shipper : GFxxxx | GRTgaz shipper code |
| 6 | Nom de l’expéditeur / Name of the shipper | AN | X |  | Text | Y | Nom de l’expéditeur / Name of the shipper : YYYY | Name of the shipper |
| 7 | Date de mise à jour / Last update | D | X | Date | DD/MM/YYYY HH:mm:SS | Y | Date de mise à jour / Last update : 17/07/2010 15:54:12 | File generation date as follows : DD/MM/YYYY HH:mm:SS |
| Daily section (for Metering Notice publication only) (1 lign with column labels separated by semi-colons, then 1 lign for each PCE/JG /metering type) |
| 1 | "Code PCE / Metering point code" | AN | X |  | Text | Y |  | Metering Point code |
| 2 | "Libellé PCE / Metering point label" | AN | X |  | Text | Y |  | Metering Point label |
| 3 | "Code PLI / Delivery station code" | AN | X |  | Text | Y |  | Delivery Station code |
| 4 | "Libellé PLI / Delivery station label" | AN | X |  | Text | Y |  | Delivery Station label |
| 5 | "Journée gazière / Gasday" | D | X | Date | DD/MM/YYYY | Y | Ex : 17/07/2010 | JG as follows: DD/MM/YYYY |
| 6 | "Redressement / Rectification" | AN | X |  | Boolean | Y | N | Constant |
| 7 | "Type de mesure / Metering type" | AN | X |  | Text | N | VOLUME ENERGIE PCS DENSITE MASSE TX_CO2 TX_N2 TX_CH4 INDICE_WOB TX_C2H6 TX_C3H8 TX_C4H10_ISOB TX_C4H10_NBU TX_C5H12_NEOP TX_C5H12_ISOP TX_C5H12_NPE TX_C6P TX_HYD | Metering type |
| 8 | "Unité / Unit" | AN | X |  | Text | N | m3(n) kWh à 0°C kWh à 0° C/m3(n) Sans unité kg/m3(n) pourcentage molaire | Metering unit |
| 9 | "Date et Heure de Mise à jour / Update date and time" | D | X | Date | YYYY-MM-DDTHH:MM:SSZ | N | 2010-07-17T14:54:39Z | Update Time |
| 10 | "Nouvelle mesure / New" | AN | X |  | Boolean | N | Y, N | New metering indicator |
| 11 | "Valeur / Value" | N | 9 |  | Float | N |  | Metering value |
| 12 | "Qualité / Quality" | AN | X |  | Text | N | A (Acquis) AF (Fiable) AD (Douteux) RI (Remodulé à partir d’un index) RF (Remodulé suite à un forçage) EM (Estimé manuellement) EA (Estimé automatiquement) AA (Acquis en alarme) F3 (forçage type 3) Bp (forçage bipasse) ... | Metering quality (indicative data) |
| Hourly section (1 lign with column labels separated by semi-colons, then 1 lign for each PCE/JG /metering type) |
| 1 | "Code PCE / Metering point code" | AN | X |  | Text | Y |  | Metering Point code |
| 2 | "Libellé PCE / Metering point label" | AN | X |  | Text | Y |  | Metering Point label |
| 3 | "Code PLI / Delivery station code" | AN | X |  | Text | Y |  | Delivery Station code |
| 4 | "Libellé PLI / Delivery station label" | AN | X |  | Text | Y |  | Delivery Station label |
| 5 | "Journée gazière / Gasday" | D | X | Date | DD/MM/YYYY | Y | Ex : 17/07/2010 | JG as follows: DD/MM/YYYY |
| 6 | "Redressement / Rectification" | AN | X |  | Boolean | Y | N | Constant |
| 7 | "Type de mesure / Metering type" | AN | X |  | Text | N | VOLUME ENERGIE PCS | Metering type |
| 8 | "Unité / Unit" | AN | X |  | Text | N | m3 kWh à 0°C kWh/m3 | Metering unit |
| 9 | "Date et Heure de Mise à jour / Update date and time" | D | X | Date | YYYY-MM-DDTHH:MM:SSZ | N | 2010-07-17T14:54:39Z | Update time |
| 10 | "Nouvelle mesure / New" | AN | X |  | Boolean | N | Y, N | New metering indicator |
| 11 | "Valeur / Value" | N | 9 |  | Float | N |  | Metering value |
| 12 | "Qualité / Quality" | AN | X |  | Text | N | A (Acquis) AF (Fiable) AD (Douteux) RI (Remodulé à partir d’un index) RF (Remodulé suite à un forçage) EM (Estimé manuellement) EA (Estimé automatiquement) AA (Acquis en alarme) F3 (forçage type 3) Bp (forçage bipasse) ... | Metering quality (indicative data) |
| 13 | "Heure / Hour" | D | X | Date | HH:MM | Y | 06:00 | Hour |

## XML format

The AM and AMJ file in the XML format is described as follows:

Finally the file composing the xsd for the AM and AMJ exchanges:

File sample in csv format :

File sample in xml format :

# Text boxes

The files naming conventions and the description of the file in csv format have been changed since the draft version of this guide.