Capacity Overruns Statement

This section describes the exchange format for data relating to the Capacity Overruns Statement, in short referred to as "BDEP” for the provisional version, “BDED” for the definitive version and “BDER” for the rectified version.

# FILE DEFINITION

The provisional Capacity Overruns Statement contains the totality of the provisional capacity overruns and allocations, as well as the subscribed operational capacities associated, for all the days of the current month M (1st/M at D/M, published on day D+1). It deals only with PCR types PLC and PLCd.

The definitive Capacity Overruns Statement contains the totality of the definitive capacity overruns and allocations, as well as the subscribed operational capacities associated, for each gas day of M. It is published at the beginning of M+1.

It deals with PCR types PLC, PLCd, PITD, ZS and PIRR.

Finally, the definitive statement contains Additional Quantities at PITTM (Extra Monthly Allocation of Daily Entry Capacity at a Transport LNG Terminal Interface Point).

The rectified Capacity Overruns Statement  contains, for a gas month M, the rectified datas related to validated rectifications, and the definitive datas for the gas days not concerned by any rectification. It is published in M+n after validation of rectified allocations.

It deals with PCR types PLC, PLCd, PITD, ZS and PIRR.

Finally, the rectified statement contains Additional Quantities at PITTM.

# WHERE TO FIND THE DOCUMENT(s)

The BDE files can be downloaded from the TRANS@ctions web portal via the publication search page:

# File name and format

The file is published in the CSV and XML formats.

It will be named according to the following rule:

| No. | Designation | Type | Length | Format |
| --- | --- | --- | --- | --- |
| 1 | Mode of exchange | Alphanumeric | 4 | BDEP, BDED or BDER |
| 2 | Contract code | Alphanumeric |  |  |
| 3 | Gas month | Date | 6 | YYYYMM |
| 3 | Date | Date | 14 | DDMMYYYYhhmmss |
| 4 | Extension | Alphanumeric | 4 | .csv ou .xml |
| 5 | Separators |  | 4 | « _ » |

In consequence, the final complete file name will be:

BDEP_CODECONTRAT_ DDMMYYYYhhmmss.csv

BDEP_CODECONTRAT_ DDMMYYYYhhmmss.xml

Or

BDED_CODECONTRAT_ DDMMYYYYhhmmss.csv

BDED_CODECONTRAT_ DDMMYYYYhhmmss.xml

Or

BDER_CODECONTRAT_ DDMMYYYYhhmmss.csv

BDER_CODECONTRAT_ DDMMYYYYhhmmss.xml

# FILE Description

## CSV format

The tables presented in this section contain the following columns:

- No.: No. of field in the line

- Name: description of field content

- Type: type of field

- Length

- Unit

- Format: Data format.

- Compulsory: determines whether the field is mandatory or not; if not, the field is kept empty.

- Value: type of values specific to the data or example(s) of values.

- Comment: additional information.

In the following tables, the types of values are as follows:

- N: numeric

- X, AN: alphanumeric

- D: date

- H: time

- E: 1-character enumeration.

The length is given within brackets where applicable:

- X(n) is a sequence of n alphanumeric characters,

- 9(n) is a sequence of n numeric characters,

- S9(n) is a numeric sequence with sign + or -.

The decimal separator is a dot.

| No. | Name | Type | Length | Unit | Format | Compulsory | Example | Comment |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Service data header (each part on 1 line) |
| 1 | Bordereau de Dépassements de Capacité Provisoire / Provisional Capacity Overruns Statement OU Bordereau de Dépassements de Capacité Définitif / Definitive Capacity Overruns Statement OU Bordereau de Dépassements de Capacité Redressé / Rectified Capacity Overruns Statement | AN | X |  | LIBELLE_FLUX_FR / LIBELLE_FLUX_EN : CODE_FLUX-x | Y | Bordereau de Dépassements de Capacité Provisoire / Provisional Capacity Overruns Statement : BDEP-123456789 Bordereau de Dépassements de Capacité Définitif / Definitive Capacity Overruns Statement : BDED-123456789 Bordereau de Dépassements de Capacité Redressé / Rectified Capacity Overruns Statement : BDER-123456789 | BDEP-x BDED-x BDER-x where x refers to an order number |
| 2 | Réseau / Network | AN | X |  | Text | Y | Réseau / Network : GRTgaz | Constant |
| 3 | Période / Period | D | X |  | DD/MM/YYYY hh:mm - DD/MM/YYYY h:mm | Y | Période / Period : 01/07/2010 06:00 – 17/07/2010 06:00 | Beginning and end publication dates |
| 4 | ID contrat / ID contract | AN | X |  | Text | Y | ID contrat / ID contract : GFxxxx01 | GRTgaz ref. no. for the contract |
| 5 | ID expéditeur / ID shipper | AN | X |  | Text | Y | ID expéditeur / ID shipper : GFxxxx | GRTgaz shipper code « nc » in case of an industrial or parent company |
| 6 | Nom de l’expéditeur / Name of the shipper | AN | X |  | Text | Y | Nom de l’expéditeur / Name of the shipper : YYYY | Name of the shipper « nc » in case of an industrial or parent company |
| 7 | Date de mise à jour / Last update | D | X | Date | DD/MM/YYYY h:mm:ss | Y | Date de mise à jour / Last update : 17/07/2010 15:54:12 | File generation date |
| Daily section (1 lign with column labels separated by semi-colons, then 1 lign for each PCR/JG ) |
| 1 | ID point contrat / ID service point | AN | X |  | Text | Y |  | Contractual Point code |
| 2 | Type de PCR / PCR type | AN | X |  | Text | Y | Example: PITD | Contractual Point type |
| 3 | Libellé / Label | AN | X |  | Text | Y |  | Contractual Point label |
| 4 | Sens / Direction | AN | X |  | Text | Y | REC, DEL | Contractual Point direction |
| 5 | Journée gazière / Gasday | AN | X | Date | DD/MM/YYYY | Y | Example: 17/07/2010 | JG |
| 6 | Qté réalisée (kWh à 25°C) / Allocated qty (kWh at 25°C) | N | 9 | kWh 25°C | Integer | Y |  | Allocation |
| 7 | Qté réalisée (kWh à 0°C) / Allocated qty (kWh at 0°C) | N | 9 | kWh 0°C | Float | Y |  | Allocation |
| 7 | Capacité Opérationnelle Souscrite (kWh à 25°C) / Operationnal Subscribed Capacity (kWh at 25°C) | N | 9 | kWh 25°C | Integer | Y |  | Daily Subscribed Operational Capacity(Delivery Capacity in case of PLC(d)/PITD/PIRR, Exit Capacity in case of ZS and Transmission Capacity in case of PITTM) |
| 9 | Capacité Opérationnelle Souscrite (kWh à 0°C) / Operationnal Subscribed Capacity (kWh at 0°C) | N | 9 | kWh 0°C | Float | Y |  | Daily Subscribed Operational Capacity(Delivery Capacity in case of PLC(d)/PITD/PIRR, Exit Capacity in case of ZS and Transmission Capacity in case of PITTM) |
| 10 | Dépassement de capacité journalier (kWh à 25°C) / Daily capacity overrun (kWh at 25°C) | N | 9 | kWh 25°C | Integer | Y |  | Daily Overrun value kWh at 0°C(Additional Quantity in case of PITTM) |
| 11 | Dépassement de capacité journalier (kWh à 0°C) / Daily capacity overrun (kWh at 0°C) | N | X | kWh 0°C | Float | Y |  | Daily Overrun value kWh at 25°C(Additional Quantity in case of PITTM) |
| 12 | Montant du Dépassement (€) / Overrun amount (€) | N | X | € | Integer | N |  | Valuation of Daily Overrun in € |
| 13 | Nouveau Dépassement / New | N | X |  | Boolean | Y | Y, N | New overrun indicator |
| 14 | Version / Version | AN | X |  | Integer | Y |  | Overrun version |
| 15 | Statut / Status | AN | X |  | Text | Y | PRO, DEF, RED | Overrun status |
| 16 | Date et Heure de Mise à jour / Update date and time | D | X | Date | YYYY-MM-DDTHH:MM:SSZ | Y | 2010-07-17T14:54:39Z | Update time |
| Hourly section – optional (1 lign with column labels separated by semi-colons, then 1 lign for each PCR/JG/hour – in case of PLC(d) only) |
| 1 | ID point contrat / ID service point | AN | X |  | Text | Y |  | Contractual Point code |
| 2 | Type de PCR / PCR type | AN | X |  | Text | Y | Example: PLC | Contractual Point type |
| 3 | Libellé / Label | AN | X |  | Text | Y |  | Contractual Point label |
| 4 | Sens / Direction | AN | X |  | Text | Y | REC, DEL | Contractual Point direction |
| 5 | Journée gazière / Gasday | AN | X | Date | JJ/MM/AAAA | Y | Example: 17/07/2010 | JG |
| 6 | Heure / Hour | D | X | Date | hh:mm - hh:mm | Y | 02:00 - 06:00 | Hour |
| 7 | Qté réalisée (kWh à 25°C) / Allocated qty (kWh at 25°C) | N | 9 | kWh 25°C | Integer | Y |  | Hourly allocation(four-hour average) |
| 8 | Qté réalisée (kWh à 0°C) / Allocated qty (kWh at 0°C) | N | 9 | kWh 0°C | Float | Y |  | Hourly allocation(four-hour average) |
| 9 | Capacité Opérationnelle Souscrite (kWh à 25°C) / Operationnal Subscribed Capacity (kWh at 25°C) | N | 9 | kWh 25°C | Integer | Y |  | Daily Subscribed Operational Capacity (Delivery Capacity) |
| 10 | Capacité Opérationnelle Souscrite (kWh à 0°C) / Operationnal Subscribed Capacity (kWh at 0°C) | N | 9 | kWh 0°C | Float | Y |  | Daily Subscribed Operational Capacity (Delivery Capacity) |
| 11 | Dépassement de capacité horaire (kWh à 25°C) / Hourly capacity overrun (kWh at 25°C) | N | 9 | kWh 25°C | Integer | Y |  | Hourly Overrun value |
| 12 | Dépassement de capacité horaire (kWh à 0°C) / Hourly capacity overrun (kWh at 0°C) | N | X | kWh 0°C | Float | Y |  | Hourly Overrun value kWh at 0°C |
| 13 | Montant du Dépassement (€) / Overrun amount (€) | N | X | € | Integer | N |  | Valuation of Hourly Overrun in € |
| 14 | Nouveau Dépassement / New | N | X |  | Boolean | Y | Y, N | New overrun indicator |
| 15 | Version / Version | AN | X |  | Integer | Y |  | Overrun version |
| 16 | Statut / Status | AN | X |  | Text | Y | PRO, DEF, RED | Overrun status |
| 17 | Date et Heure de Mise à jour / Update date and time | D | X | Date | YYYY-MM-DDTHH:MM:SSZ | Y | 2010-07-17T14:54:39Z | Update time |

Note : hourly overruns are calculated with four-hour average of hourly allocations. Therefore, it may be up to 21 hourly overruns for each gas day / PCR.

## XML format

The BDE file in the XML format is described as follows :

Finally the file composing the xsd for the BDE exchanges

File sample in csv format :

File sample in xml format :